## Slide 1
ONLINE SEMINAR 2
The pathway to a carbon cycle economy:
Green CO2 potentials and valorization
1

## Slide 2: CO2 – from emission to feedstock
Simple classification of pathways for CO2 reuse
Source: Energieinstitut an der JKU based on IEA 2019
Food & Drinks
Welding Technology
Medical applications
Heat transfer medium
Refrigeration technology
Supercritical combined heat and power generation
Solvents
Enhanced oil recovery (EOR)
Decaffeination
dry cleaning
Fertilization
Greenhouses
Algae Cultivation
Urea
DIRECT USE
CONVERSION
Industrial processes
Underground storage
Air
Biomass
Fossil fuels
Fuels
Methane
Methanol
Petrol/diesel/kerosene
Chemicals
Intermediates (methane, methanol)
Polymers (Plastics)
Materials
Aggregates (fillers)
Cement
Concrete
Notes: CO2 is unquestionable the biggest threat to global climate but the carbon and oxygen containing gas has also its industrial applications that are already established applications especially in the field of direct use not just bringing the bubbles to the drinks but also als solvent in enhanced oil recovery or as heat carrier and others. In the last years significant development efforts on new fuels, chemicals and materials from CO2 were made and the top start ups in the field recieved funding of 100 mio USD+

## Slide 3: CO2 as valuable commodity
Growth in global demand
Growth in global demand of CO2 over the years (left); breakdown of demand in 2015 (right)
Chart: worldwide CO2 use in Mt/year
| 2000 | 2015 | 2020 | 2025
 | 150 | 230 | 250 | 272
Chart: 
| urea | EOR | beverages | food | fab metal | other
 | 57 | 34 | 3 | 3 | 2 | 4
Source: Energieinstitut an der JKU based on IEA 2019, ETC (2018); IHS Markit (2018); US EPA (2018)
Notes: some of these efforts can already be quantified, the growth rates show an upward trend with a current volume of approx. 250 million T CO2 use in Mt/year. but in relation to the level of emissions, there is clearly still almost a factor one thousand in between, talking about mega and giga tons & not accounted for in the GHG balances

## Slide 4: CCU – Carbon Dioxide Capture and Utilisation
CO2 + water conversion = inverted oxidation / combustion = intrinsically energy demanding
Product |  | 
Methane (g) | CH4 | 801
Acetylene (g) | C2H2 | 1,227
Ethanol (liq) | C2H6O | 1,301
Ethen (g) | C2H4 | 1,314
Ethane (g) | C2H6 | 1,442
Propane (g) | C3H8 | 2,074
Butane (g) | C4H10 | 2,703
Octane (liq) | C8H18 | 5,219
Product |  | 
Methane (g) | CH4 | 801
Acetylene (g) | C2H2 | 1,227
Ethanol (liq) | C2H6O | 1,301
Ethen (g) | C2H4 | 1,314
Ethane (g) | C2H6 | 1,442
Propane (g) | C3H8 | 2,074
Butane (g) | C4H10 | 2,703
Octane (liq) | C8H18 | 5,219
energy
demand
CO2
Hydrocarbons
Industrial chemicals
Carbohydrates
Carbonates
Urea
Mimimum energy demand for conversion of CO2 to products
Converting CO2 is generally energy intensive
Also catalysed conversion fight against the 2nd principle of thermodynamics
Carbonates are special, kinetics can partly offset thermodynamic benefits
Notes: CCU technologies developed now will certainly see a net zero carbon world, because • Expected time to market: decade(s) • Expected time to build CCU infrastructure: decade(s) • Economic life time: decades

## Slide 5: An objective view on the entire process chain
Approximated system efficiencies
CO2 used ≠ CO2 avoided
CCU products are not carbon neutral of circular by default
Methane (g) | CH4
Methanol (liq) | CH3OH
Source: based on Mijndert van der Spek ETH Zürich, 20.04.2020, Dias, V. et al. Front. Mech. Eng., 29 May 2020, Bergins, C., et al. POWER-GEN Europe 2015,
There is much
room to improve
CCU efficiencies
Efficient hydrogen provison is a key enabler for maximized efficiency
CCGT … Combined Cycle Gas Turbine
PCC … Post Combustion Capture
DAC … Direct Air Capture
Notes: CCU fuels are circular nor carbon neutral by default • Need to be net zero CO2 to be succesful à DAC or BECC • High efficiency cost of seasonal power storage • power-CH4-power: η ~ 30% • power-MeOH-propulsion: η ~ 13% • Hydrogen most efficient; CCU needs total system analysis to evaluate its potential performance in future energy systems

## Slide 6: The CO2EXIDE project approach
The project aims for sustainable environmentally friendly products, thus the focus is on biogenic CO2 and renewable electricity as main resources. As cost are a determining factor, further focus is on existing, high-purity CO2-sources such as:
Biogas upgrading
Bioethanol production
P2X/CCU technologies can balance future energy systems with high shares of fluctuating renewable energy sources such as:
Photovoltaics (PV)
Wind power
Thus, the focus is on existing large PV and wind farms.
Renewable inputs for sustainable process design

## Slide 7: Potential sources of biogenic CO2
existing, high-purity point sources in the focus
CO2-sources
with ratio of CO2
in the off-gas
Most important biogenic sources
are highlighted in green
Source: Rodin, V. et al. (2020) Assessing the potential of carbon dioxide valorisation in Europe with focus on biogenic CO2, Journal of CO2 Utilization, Vol. 41, 101219

## Slide 8: Biogas plant distribution in Europe
existing, high-purity point sources in the focus
Biogas plant distribution in Europe at the end of 2017
European country ranking according to the number of biogas upgrading plants in early 2017
Source: Rodin, V. et al. (2020) Assessing the potential of carbon dioxide valorisation in Europe with focus on biogenic CO2, Journal of CO2 Utilization, Vol. 41, 101219
Chart: number of biogas plants
| Germany | Italy | France | Switzerland | UK | Czech Rep. | Austria | Poland | Netherlands | Spain | Sweden | Belgium | Slovakia | Denmark | Norway | Finland | Hungary | Portugal | Latvia | Greece | Lithuania | Luxembourg | Ireland | Slovenia | Croatia | Estonia | Cyprus | Bulgaria | Romania | Serbia
 | 10971 | 1655 | 742 | 632 | 613 | 574 | 423 | 308 | 268 | 204 | 198 | 186 | 179 | 144 | 138 | 96 | 81 | 64 | 56 | 37 | 36 | 30 | 29 | 26 | 26 | 18 | 13 | 11 | 11 | 10
10971
Chart: number of biomethane plants
| Germany | UK | Sweden | Switzerland | France | Netherlands | Denmark | Austria | Finland | Italy | Norway | Lithuania | Hungary | Iceland | Estonia
 | 194 | 85 | 63 | 31 | 30 | 26 | 22 | 15 | 12 | 7 | 4 | 3 | 2 | 2 | 1

## Slide 9: Biogenic CO2 from biomethane production
existing, high-purity point sources in the focus
CO2 potential in Mt/year from biomethane upgrading as part of total CO2 potential from biogas production for the EU-28 (data for 2016)
Source: Rodin, V. et al. (2020) Assessing the potential of carbon dioxide valorisation in Europe with focus on biogenic CO2, Journal of CO2 Utilization, Vol. 41, 101219
approx. 500 biogas upgrading plants to biomethane in operation in Europe
14 % of biogenic CO2 from biogas is already separated, but hardly utilized
Significant potential of highly concentrated biogenic CO2 for valorization
Chart: 
| Biomethane upgrading | Further potential biogas
Carbon Dioxide [million tons / year] from biomethane production for the EU-28 | 3.1417 | 20.0068
3.15 Mt/yr
20.00 Mt/yr

## Slide 10: Biogenic CO2 from bioethanol fermentation
existing, high-purity point sources in the focus
CCU technically feasible without extensive effort
Some production site capture the CO2 already distribute the produced CO2 commercially
    Dry ice
    Carbonic acid for beverages
    Fertilizer for greenhouses
Amount of CO2 in Mt/year produced in the EU bioethanol industry in
2016 including amount of possibly commercialized CO2
Source: Rodin, V. et al. (2020) Assessing the potential of carbon dioxide valorisation in Europe with focus on biogenic CO2, Journal of CO2 Utilization, Vol. 41, 101219
Chart: 
| Commercially utilized (projection) | Further potential bioethanol (CO2 utilization unkown)
Carbon Dioxide [million tons / year] from bioethanol fermentation for the EU-28 | 2.0345 | 3.6783
2.03 Mt/yr
3.68 Mt/yr
∑ 5.71 Mt CO2/yr

## Slide 11: CO2 capture
Capture costs
CO2 from biogenic sources can provide lowest capture costs
Direct Air Capture (DAC) is expected to rapidly reduce its costs
Chart: CO2 source
| biomass / wastewater treatment | bioethanol plant | direct air capture | chemical industry | refinery | iron&steel industry | cement industry | fossil power plant
min | 0 | 5 | 80 | 13.3 | 44 | 16 | 24.7 | 19
Q1 | 3.75 | 8.5825 | 70.3759 | 0.05 | 6.75 | 12.5875 | 10.025 | 21.25
M | 45.75 | 7.2175 | 150.9169 | 4.65 | 3.25 | 5.5375 | 19.725 | 16.75
Q3 | 50.5 | 3.23 | 64.1207 | 4.875 | 10.75 | 15.375 | 19.05 | 15.1875
max | 30 | 87.37 | 354.0109 | 31.125 | 29.25 | 25.5 | 1.5 | 28.8125
biogenic CO2 in Europe
In total approximately 506 Mt/yr of biogenic CO2 are produced annually in Europe
Chart: 
| Solid biofuel combustion | Biogas combustion | Bioethanol production | Biogas upgrading to biomethane | Alcoholic beverages production
 | 437 | 58 | 4.3 | 3.44 | 2.92
506 | 1
Of which 86% imply cost intensive flue gas purification
Source: Energieinstitut an der JKU

## Slide 12: Matching of biogenic CO2 and RES sources
GIS-based analysis of potential CO2EXIDE production sites
Mapping of biogenic CO2 sources
    existing biomethane upgrading plants (>16 kt CO2/yr)
    existing bioethanol production sites (> 160 kt CO2/yr)
Mapping of RES sources
    Existing onshore wind farms > 1 MW
    Existing solar power plants > 1 MW
Focus on 4 categories of plant sizes from 1 to 500 MW
Based on GIS analysis tools, existing CO2 and renewable power sources were matched to identify possible CO2EXIDE production sites within Europe to …
… provide 100 % renewable based products
… avoid transport of (hazardous) reagents
… support grid operation by balancing out fluctuating, locally generated renewable energy
For the specific case studies, additionally favorable infrastructure was considered…
…ethylene producers/consumers
…pipeline infrastructure

## Slide 13: GIS based approach for roll-out scenarios
Visualisation & intersection of CO2-point soures and renewable power plants
Source: Energieinstitut an der JKU
3 case studies in 3 countries concidering local conditions, existing infrastuctures

## Slide 14: Development of specific case studies for potential technology roll-out
Modelling of fluctuating renewable power generation
Typical electricity production characteristic of a 1 MW photovoltaic power plant (top) & wind farm (bottom)
The power is divided in the share of grid feed-in and power for the potential CO2EXIDE-plant for scenario development; central european conditions applied
minimum levelized cost of CCU product
avoidance of usage competition & system inefficiencies
Source: Energieinstitut an der JKU

## Slide 15: For takeway…
CCU, a promising option for CO2 emission reductions
CO2 use is a complement, not an alternative to large-scale emissions reductions.
The scientific and technical challenges in the reductive activation, catalytic technologies for CO2 conversion to fuels and chemcials is a dynamic field.
Achieving a net zero emissions EU energy system by 2050 based on predominantly renewables is a prerequisite.
In absence of binding international climate agreements, a sufficient high price on CO2 emissions, CCU is actually hardly economic.
Nevertheless the need to identify the range of future-proof CCU technologies and products now due to the expected long periods to market.
As with all renewables scale up and market division needs to be linked to stringent sustainability criterias to take full advantage. A framework for analysis is currently evolving.

## Slide 16: Our European projects in the area of technology assessments
Energy Institute activities in process assessment

## Slide 17
Many thanks for your attention!

## Slide 18: Further Information
Project coordination
Arne Roth arne.roth@igb.fraunhofer.de
Fraunhofer IGB
Nobelstrasse 12, 70569 Stuttgart
Germany
Contact
Johannes Lindorfer
lindorfer@energieinstitut-linz.at
Energy Institute at the Johannes Kepler University Altenberger Strasse 69, 4040 Linz Austria
www.CO2EXIDE.eu